## Slide 1
Outputs
smin, smax
s0, umax
e (mm/t)
Qreg_rel
envmin (ML/t)
I (ML/t)
d (ML/t)
None: [ ]
Time series : array
Policy function: dict
None: [ ] → Qreg_rel = d
Time series : array
Policy function: dict
s (ML)
E (ML/t)
env (ML/t)
spill (ML/t)
Inputs
Mass balance function
Regulated inflows
Qreg
[inflows]
Regulated releases
Qreg [releases]
Regulated flows
Qreg
None: [ ]
Policy function: dict, dict
Regulated inflows + releases
Qreg [rel_inf]
Qreg_rel (ML/t)
Mass balance function
envmin ≥
inf
Yes
No
env =
inf
envmin ≥
sto + inf - E
No
env =
sto + inf - E
env ≥
envmin
Yes
Qreg_rel = min(Qreg_rel ,
sto + inf - E – env)
Qreg_inf
spill = max(0,
s + inf - E – env + Qreg_rel – smax)
st+1 = max(smin,
s + inf - E - env + Qreg_rel - spill)
1. Environmental flow
2. Regulated releases
3. Spill
4. Storage
sto = s – smin
inf = I + Qreg_inf
d = demand
env = environmental flow
env_min = minimum env
s = storage volume
smin = min storage
smax = max storage
s0 = initial storage
Qreg = regulated flow
Qreg_inf = regulated inflow
Qreg_rel = regulated release
umax = max release
I = natural inflow
e = evaporation per unit area
A = storage surface area
E = e * A = evaporation
Res_sys_sim diagram